## Slide 1: ST67W611 Wi-Fi 6 + Bluetooth® LE + Thread
Santa Clara Wireless Team

## Slide 2: Agenda
#
#
How to use X-CUBE-ST67W61 within STM32CubeMX
(Walk-through)
#
Device Setup and Flashing
#
#
Documentation
Walk through of the MQTT application
X-Cube- ST67W61 Package
Introduction to MLC
#
#
Demo: MLC Workflow in MEMS Studio
MQTT Hands-On
Integrating MLC into ST67 MQTT Demo
#

## Slide 3: Prerequisites
X_CUBE_ST67W61_V1.0.0
STM32CubeIDE v1.16.1+
STM32CubeProgrammer v2.18.0+
STM32CubeMX v6.14.1+
HyperTerminal – TeraTerm v.5.4.0
Python v.3.12.7+
STBLE Toolbox
IoT MQTT Panel App

## Slide 4: Installing X-CUBE-ST67W61
Open STM32CubeMX with admin rights
Go to “Install/Remove” software packages
Under STMicroelectronics tab
Install the X-CUBE-ST67W61
1
2
3

## Slide 5: STM32U5 and X-CUBE-FREERTOS
Download latest STM32U5
Download latest X-CUBE-FREERTOS

## Slide 6: X-Cube-ST67W61

## Slide 7: X-CUBE-ST67W61 package overview
Board support package
CMSIS libraries
Device HAL drivers
APIs include files
Templates for middleware and driver config files
Integration between generic API and driver
W61 driver
AT commands / responses
SPI driver
UART Output logs
Memory usage statistics
CLI Console
STM32CubeIDE and EWARM Project Files
X-CUBE-ST67W61 Overview - stm32mcu
Variety of Nucleo hosts
Notes: With the X-Cube package downloaded and installed the directory should appear as shown.
The X-Cube package for the ST67W61 contains all the necessary source code and projects to generate binaries running on the STM32 host, Nucleo-U575ZI-Q.
Command Line Interface and Echo applications are also provided for the Nucleo-H7S3L8, Nucleo-H563ZI and Nucleo-N657X0 hosts.
The ST67W6X_Network_Driver source files are provided within the middlewares folder:
The network driver includes the API include files, SPI driver, as well as the AT command formatting interface.
In the ST67W6X_Utilities folder under projects the binaries for programming the ST67W611M1 module are also provided.

## Slide 8: X-CUBE-ST67W1 middleware
All the above submodules make use of FreeRTOS™
 | Scope / description
W61_bus | This is the SPI driver for communication between the host and the ST67W61.
W61_at | It does the formatting of the AT commands to be sent and it implements a receive tasks to decode the received messages from the W61 and dispatch them to the correspondent module.
W6x service API | The Core directory implements an adaptation layer between the W61 AT driver and the API proposed to the application. The APIs are "Zephyr-like" for the Wi-Fi® and socket API for the network operations.
Utils | Console handling, debug, trace, performance measurements.
Notes: The ST67W6x Network driver files are provided within the middlewares folder of the X – cube package.
There are 4 key components that enable the interface and command sets for the ST67W6x network driver.
W61_bus – The SPI driver for communication between the hsot and the ST67W61
W61-at – the formatter for the AT commands issued by the host MCU and the response from the ST67W61.
W6x service API – Core directory for implementing AT commands from the host MCU.
Utils – contains the logging, debugging, and performance measurement components
All of the above submodules make use of FreeRTOS.

## Slide 9: X-CUBE-ST67W1 AT Commands
The command set includes basic AT commands, Wi-Fi function AT commands, TCP/IP toolbox AT commands, and Bluetooth® LE related AT commands.
There are two types of AT messages returned from the AT command port: AT responses messages and AT message reports:
Response Messages: Each AT command input returns response messages to tell the sender the result of the AT command.
The last message of a response will always be either "OK" or "ERROR".
Connectivity:ST67W611M AT Command - stm32mcu
Notes: The ST67W6x Network driver files are provided within the middlewares folder of the X – cube package.
There are 4 key components that enable the interface and command sets for the ST67W6x network driver.
W61_bus – The SPI driver for communication between the hsot and the ST67W61
W61-at – the formatter for the AT commands issued by the host MCU and the response from the ST67W61.
W6x service API – Core directory for implementing AT commands from the host MCU.
Utils – contains the logging, debugging, and performance measurement components
All of the above submodules make use of FreeRTOS.

## Slide 10: X-CUBE-ST67W1 AT Commands cont...
2. Message Reports : AT will report important state changes or messages in the system.
Connectivity:ST67W611M AT Command - stm32mcu
Notes: The ST67W6x Network driver files are provided within the middlewares folder of the X – cube package.
There are 4 key components that enable the interface and command sets for the ST67W6x network driver.
W61_bus – The SPI driver for communication between the hsot and the ST67W61
W61-at – the formatter for the AT commands issued by the host MCU and the response from the ST67W61.
W6x service API – Core directory for implementing AT commands from the host MCU.
Utils – contains the logging, debugging, and performance measurement components
All of the above submodules make use of FreeRTOS.

## Slide 11: API Documentation
Found in \Middlewares\ST\ST67W6X_Network_Driver\Doc
API Definitions
Overview of API calls
Correlated AT Commands

## Slide 12: API Documentation cont…
Selecting w6x_wifi.c will provide the different API categories
Selecting the API, W6X_WiFi_Scan(), will provide information and the call graph

## Slide 13: X-CUBE-ST67W61 applications
 | Scope / description
Bluetooth® LE commissioning | Uses Bluetooth® LE to provide Wi-Fi® SSID and password after scanning available AP
Bluetooth® LE p2p client | Point-to-Point communication demo using Bluetooth® LE (GATT Client)​ Scan and connect to a p2pServer​ Write messages & receive notifications from the p2pServer
Bluetooth® LE p2p server | Point-to-Point communication demo using Bluetooth® LE (GATT server)​ Advertises and wait for a connection from either:​ - p2pClient app​ - ST BLE Toolbox smartphone application
Echo | TCP Echo feature over Wi-Fi​ - Good starting point for generic user development
CLI | ST67 evaluation via CLI and for WTS tests the Wi-Fi solution. Wi-Fi API: scan, connect, disconnect, etc NET socket API and iperf Bluetooth® LE API
Echo FOTA | FOTA (firmware update over-the-air) feature demo over Wi-Fi​ - Using HTTP
HTTP server | HTTP server over Network API​ The server, running on the host board, has been validated with 1 client, using HTTP requests to send and receive data to and from the server.
HTTPS client | HTTPS Client over Network API demo​ - Basic GET requests to retrieve worldwide weather reports
Wi-Fi® commissioning | Wi‑Fi® commissioning project using an HTTP server, hosted by a device configured as a soft access point (SoftAP) and station (STA).
MQTT Demo | Starting point for MQTT user development​ - Sends IKS sensor data to an MQTT broker
Notes: There are a number of different example applications that are available within the X-cube package.
Applications delivered with the XCubeST67W6x package are provided with both STM32CubeIDE and EWARM project files.
The applications provided outline different BLE and WiFi use cases
BLE Commissioning is an example for providing WiFi credentials through BLE.
The Echo application is the starting point for application development and demonstrates TCP echo feature over WiFi.
CLI is the command line interface developed to evaluate and test the ST67
Echo FOTA application demonstrates the firmware update over the air feature utilizing WiFi
MQTT Demo demonstrates cloud connectivity by providing data to a remote broker.

## Slide 14: Echo Application
Echo application is the starting point for WiFi application development for the ST67W61 within the X-Cube-ST67W6x pack.
Within the application code the initial API calls can be seen:
W6X_Init() – Initialize driver for ST67W6X
W6X_WiFi_Init() – Initialize ST67W6X WiFi module
W6X_WiFi_SetDTIM() - Set DTIM value
(dtim * 100ms). 0: Disabled, 1: 100ms, 10: 1s
W6X_Net_Init() – Initialize ST67W6X Network module
W6X_WiFi_Scan() – Scan and list all nearby APs
Etc.

## Slide 15: X-CUBE-ST67W1 NCP tools
Tool | Description
NCP_get_chip_info.bat | Script to retrieve ST67 MAC address and locking information even if no firmware is loaded onto the ST67 device.
NCP_update_mfg.bat | Script to flash the ST67 module with the manufacturing application.
NCP_update_mission_profile.bat | Script to flash the ST67 module with the mission profile application.
Scripts for flashing the latest mission or manufacturing firmware:​
..\x-cube-st67w61-v1.0.0\Projects\ST67W6X_Utilities\Binaries
Notes: The X-Cube package comes with binaries and tools necessary for flashing the ST67W611M1.
The programming process can be automated using the included batch scripts provided within the X-cube package along with STM32CubeProgrammer
The different batch scripts automate different processes related to the ST67W611M1 device.
NCP_get_chip_info.bat retrieves information from the ST67 such as MAC address and locking information
NCP_update_mfg.bat script flashes the ST67 module with the manufacturing application that is used for RF evaluation
NCP_update_mission_profile.bat flashes the ST67 module with mission profile application that is used for normal application and development purposes.

## Slide 16: ST67W611M Security Overview
Two modes, each with a header containing a digital signature and versioning info
Mission mode:
  Bootloader binary
    Authenticated by the ROM code during initial boot process
    Versioning info to prevent rollback
  Mission profile binary
    Wi-Fi® & Bluetooth® LE binary used for operational tasks
    Authenticated by bootloader to ensure integrity & authenticity before execution
Manufacturing mode:
  Bootloader binary
    Authenticated by the ROM code during initial boot process
    Versioning info to prevent rollback
  MFG firmware binary
    Used for test and production configuration
    Authenticated by bootloader to ensure integrity & authenticity before execution
Connectivity:ST67W611M Security Overview - stm32mcu
Notes: The ST67 binaries included within the X-Cube package come with a security enabled feature to prevent different FW from being flashed to the ST67 device.
This is done through the use of signed binaries as well anti-rollback mechanisms that prevent FW from being downgraded on the ST67.

## Slide 17: Flashing ST67 & Device Setup

## Slide 18: ST67W611M Modes of Operation Manufacturing and Mission Modes
FLASH
XTAL
ANTENNA
QCC743
UART
Manufacturing mode
  Host-less Application
  Dedicated to RF performances monitoring and calibration.
  QC provides graphical tools to control the device through the UART interface
FLASH
XTAL
ANTENNA
QCC743
Host
STM32
SPI
ST67W611M
ST67W611M
Host
STM32
STLINK-UART
Bypass Apply
ST67W611M1 BOOT and bootstrap modes - stm32mcu
Mission mode (Functional)
  Implementing the AT command for the different supported protocol (WIFI / BLE / MQTT /..) through the SPI interface.
  The ROM boot loader loads and executes the program from SPI Flash to boot the system.

## Slide 19: STM32U575 and ST67W611M configuration
NUCLEO-U575ZI-Q
1x NUCLEO-U575ZI-Q board
1x X-NUCLEO-67W61M1 board
Boards connected through Arduino® connectors
  Key signals: SPI (SCK, MISO,MOSI,CS), SPI_RDY, CHIP_EN, BOOT, UART_TX/RX
Power: MicroUSB connection to NUCLEO-U575ZI-Q
X-NUCLEO-67W61M1
Notes: The host device and ST67 must be connected with the following configuration when flashing the device with one of the Nucleo boards inherently supported by the X-Cube St67W6x package
There are a number key signals that must be connected between the host MCU and NCP for flashing and operating the ST67 in mission and mfg modes.
The key signals connected through the Arduino connectors are:
4 wire SPI (SCK, MOSI, MISO, CS)
SPI_RDY – signal notifying the host MCU that there is data on the ST67
CHIP_EN
Boot
Uart TX and RX
Power
With supported nucleo boards this can be done by interfacing the devices with the Arduino connectors.
Power in this configuration will be provided to the host MCU board and then through the Arduino connector.

## Slide 20: Nucleo-U575ZI and X-Nucleo-67W61M1 Configuration
When stacking the Nucleo and X-Nucleo boards the Arduino connectors must be aligned.
The MicroUSB port is used when programming the STM32U575 or ST67W611M1.
The MicroUSB port is also used to read the UART messages from the STM32U575 in a serial terminal.

## Slide 21: Flashing ST67W611M1 Mission Mode (Functional Mode) Setup
Using batch scripts located:
C:\ x-cube-st67w61-v1.0.0\Projects\ST67W6X_Utilities\Binaries
Nucleo-U575ZI-Q and X-Nucleo-67W61M1 stacked together
USB cable connected to microUSB port on Nucleo-U575ZI-Q and Windows PC.
Double-click the batch files to execute
  NCP_update_mission_profile.bat will flash the ST67W61M with the spi_wifi binary and the host processor with CLI application.
Prerequisites:
Installed STM32CubeProgrammer
  Installed in default directory (C:\Program Files\STMicroelectronics\STM32Cube\STM32CubeProgrammer
Installed X-CUBE-ST67W61
  Installed on C: drive (C:\x-cube-st67w61-v1.0.0)**
**Note: Path length limits and paths with spaces in them for the x-cube-st67w61-v1.0.0 may cause issues. Saving on C: drive will prevent these issues.

## Slide 22: Flashing ST67W611M1 Mission Mode (Functional Mode) Process
When executing NCP_update_mission_profile.bat the script will prompt the user with a warning message about locking the NCP. This is expected, and all devices have previously been locked with older firmware at manufacturing. Please press “Y” to continue.
The NCP_update_mission_profile.bat will have 3 sequential flashing stages. The script will flash the STM32U5 with Bootloader.bin, then the ST67 with the signed mission mode binary, and the STM32U5 with ST67W6X_CLI.bin. Please verify success of all 3 flashing stages.

## Slide 23: Flashing ST67W611M1 Mission Mode (Functional Mode) Verification
Flashing success can be verified by connecting to the Nucleo-U575ZI-Q with a serial terminal.
Configure the serial terminal with the following parameters and connect to the corresponding COM port for the Nucleo-U575ZI-Q.
With the serial terminal program configured, press the reset button the Nucleo-U575ZI-Q and verify application and SDK version.
**Note: “Manufacturing Year” date may be incorrect and populated with the year “2000”. This will have no effect on the functionality.

## Slide 24: How to use X-CUBE-ST67W61 within STM32CubeMX

## Slide 25: Software Development Tools
“STM32CubeIDE” development environment
“STM32CubeMX” initialization code generator
“X-CUBE-ST67W61” application code and drivers for Wi-Fi

## Slide 26: STM32CubeMX an All-in-1 Development Tool

## Slide 27: Installing X-CUBE-ST67W61
Open STM32CubeMX with admin rights
Go to “Install/Remove” software packages
Under STMicroelectronics tab
Install the X-CUBE-ST67W61
1
2
3

## Slide 28: STM32U5 and X-CUBE-FREERTOS
Download latest STM32U5
Download latest X-CUBE-FREERTOS

## Slide 29
Three possible cases to generate the code from the Cube MX:
Case 1: How to generate a project starting from an existing .ioc
Case 2: How to export a project to a pinout compatible MCU
Case 3: How to generate a project starting from scratch
In this section: We would be walking through to generate BLE Commissioning code using the following:
Case 1 with NUCLEO-U575ZI-Q as host processor
Case 3 with NUCLEO-G0B1RE as host processor

## Slide 30: BLE Commissioning App
This application aims to demonstrate how to provision Wi-Fi credentials via Bluetooth® LE to establish a Wi-Fi connection to an access point.
ST Web Page/ ST BLE Toolbox

## Slide 31: BLE Commissioning App cont..
The application acts as a peripheral device embedding the commissioning profile and its four characteristics.
At startup, the application starts to advertise.
ST Web Bluetooth® Interface must be used to scan and connect to the commissioning application: (Web-Interface available from the browser) / ST BLE Toolbox (Mobile Application)
Once connected, a Wi-Fi commissioning interface is available on web Bluetooth® page/ ST BLE Toolbox
Wi-Fi Commissioning Interface
Wi-Fi Scan
Wi-Fi Connect
Wi-Fi Disconnect
Wi-Fi Ping

## Slide 32: Commissioning profile overview
The Wi-Fi commissioning application demonstrates point to point communication using proprietary service and characteristics. It acts as a Peripheral device with one GATT service and four characteristics.
Wi-Fi commissioning server:
  Contains the Wi-Fi commissioning service, which exposes four characteristics: Wi-Fi Control (write), Wi-Fi Configure (write), Wi-Fi Access Point List (notification), Monitoring (Notification) to control and monitor a Wi-Fi connection.
  Is the GATT server
  Client Collector: (STBLE Toolbox/ ST Web Bluetooth page)
  Accesses the information exposed by the Wi-Fi commissioning application, configures and controls the Wi-Fi connection with the write characteristics, monitors the Wi-Fi connection status by receiving notifications from it
  Is the GATT client

## Slide 33
The table below describes the structure of the commissioning service:
Wi-Fi control characteristic:
  Used to drive the Wi-Fi by launching scans, connecting or disconnecting from a network

## Slide 34
Wi-Fi access point list characteristic:
  Used to notify information about scanned access points
Monitoring characteristic:
  Used to notify information about Wi-Fi network.
Wi-Fi configure characteristic:
  Used to setup the Wi-Fi parameters before establishing a connection

## Slide 35: Generating BLE Commissioning app using NUCLEO-U575ZI-Q as host processor (Hands-on)

## Slide 36: Case 1: Generating BLE Commissioning app using NUCLEO-U575ZI-Q as host processor
We would start with the ST67W6X_Echo.ioc file as a starting point and change the configuration to generate the BLE Commissioning application from the STM32CubeMX.
Browse through C:\X_CUBE_ST67W61_V1.0.0\Projects\NUCLEO-U575ZI Q\Applications\ST67W6X\ST67W6X_Echo
Copy ST67W6X_Echo.ioc
Create a new directory C:\ST67_Workshop
Paste and rename to ST67W6X_BLE_Commissioning.ioc
Copy &
Paste
Rename

## Slide 37: Loading ioc file in STM32CubeMX
1. Run STM32CubeMX with admin rights
2. Load Project
3. Go the ST67_Workshop
4. Select the ioc file
5. Click open
6. Migrate (If you get the warning)
7. Click Ok

## Slide 38: Configuration
1. Select Components
2. Select BLE Commissioning app
3. Under Middleware and Software Packs
4. Select X-CUBE-ST67W61
5. Disable W6X_POWER_SAVE_AUTO
(NCP in power save mode)
Note: This define must be 0 if BLE is enabled
Bluetooth Low Energy connection with NCP in Power save mode requires accurate external low-frequency clock. To setup and use external clock, SW and HW settings must be modified.
Refer to [Wiki Bluetooth LE with low-power setup](https://wiki.st.com/stm32mcu/wiki/Connectivity:How_to_measure_ST67W611M_current_consumption#Bluetooth-C2-AE_LE_with_low-power_setup) page to be informed about required changes.

## Slide 39: Project Settings
Here, we are enabling the Flat directory structure: (i.e. Driver and MW directories copied into your project directory)
1. Enable “Generate Under Root”
2. Enable “ Use Default Firmware Location”

## Slide 40: Project Settings cont..
3. Enable “Copy only the necessary files”

## Slide 41: Generate Code
4. Enable this option
(here: we are not generating this function call)
5. Generate Code

## Slide 42: STM32CubeIDE
After, generating the code, you would view similar folder structure under ST67_Workshop
Load the project on the STM32CubeIDE
Call main_app() function under StartDefaultTask() in app_freertos.c file

## Slide 43: Time to build and flash
Console after building the application
Tera Term logs after flashing the BLE Commissioning application

## Slide 44: Porting to a new host processor using STM32CubeMX

## Slide 45: Porting over new host processor(1/3)
Select the Host MCU
Choose the target STM32 part number from the STM32CubeMX
2. Check schematics of Host MCU and ST67
Review pin mappings for SPI, GPIO, USART
3. Configure USART for Debugging
Used for debugging logs via STLink virtual port
4. Configure the SPI Interface for Host MCU and ST67 communication
Set SPI pins, SPI mode
5. Configure DMA Channels for SPI
Fast and reliable SPI data transfer, reducing CPU load during transmission

## Slide 46: Porting over new host processor(2/3)
6. Configure GPIO Pins ( CHIP_EN, SPI_RDY, SPI_CS, BOOT, User_Button)
Set GPIO Mode, GPIO output level, GPIO Maximum Output speed
7. Configure SYS (Time base Source)
8. Configure Clock
9. Enable FreeRTOS Middleware
Setup default task, heap size, stack size and required priorities
10. Enable X-CUBE-ST67W61
Setup Application, W61 Drivers, Utilities
11. Configure NVIC Interrupt Settings
SPI, DMA, USART, EXTI

## Slide 47: Porting over new host processor(3/3)
12. Project Creation and Code Generation
Generate project files (STM32CubeIDE/IAR)
Open in IDE for application development
13. Application Entry: Call main_app()
Inside StartDefaultTask, invoke main_app()
This initializes ST67W6X Driver, ST67W6X Wi-Fi module, ST67W6X Network module, Application specific functions
14. Build and Flash the application

## Slide 48: Generating BLE Commissioning app using NUCLEO-G0B1RE as host processor (Walk-through)

## Slide 49: Case 3: Generating BLE Commissioning app using NUCLEO-G0B1RE as host processor
Open STM32CubeMX and create the new project.

## Slide 50
Select the board selector
Select NUCLEO-G0B1RE
Type STM32G0
Select STM32G0
Start Project

## Slide 51
Select Yes

## Slide 52: Pinout
Pin function | Arduino Connector | STM32G0 Pin | GPIO mode | GPIO pull mode | GPIO speed
SPI_CLK | CN5.D13 | PA5 | AF PP | No Pull | Very high
SPI_MISO | CN5.D12 | PA6 | AF PP | No Pull | Very high
SPI_MOSI | CN5.D11 | PA7 | AF PP | No Pull | Very high
SPI_CS | CN5.D10 | PB0 | Output PP | No Pull | high
USER_BUTTON | - | PC13 | EXTI Falling | Pull-up | N/A
CHIP_EN | CN9.D5 | PB4 | Output PP | No Pull | High
BOOT | CN9.D6 | PB14 | Output PP | No Pull | Low
SPI_RDY | CN9.D3 | PB3 | EXTI Falling/Rising | No Pull | N/A
When generating an application from scratch and if X-Nucleo-67W61M1 is used, the pinout must be set in accordance with the ST67W61M1 Arduino interfaces.

## Slide 53: Assigning functionality
For assigning, click on the pin and select functionality.
(e.g) PA5->SPI_SCK

## Slide 54: Pinout View
After, assigning all the pins mentioned from the pin out table, this would be overall pinout view

## Slide 55: UART GPIO(USART 2)
Select USART2
GPIO Settings
Parameter Settings
PA2: USART2_TX
PA3: USART2_RX

## Slide 56: SPI GPIO(SPI1)
Select SPI1
PA5: SPI_SCK
PA6: SPI_MISO
PA7: SPI_MOSI
Parameter settings

## Slide 57: DMA Channels
Select DMA
SPI1_TX -> DMA1 CHANNEL 1->High
SPI1_RX -> DMA1 CHANNEL 2-> High

## Slide 58: GPIO
Select GPIO
GPIO pin names
GPIO output level
GPIO mode
GPIO Maximum Output speed
GPIO User label

## Slide 59: Timer
Sys mode configuration: TIM1 in place of systick

## Slide 60: Clock Configuration
In the ''Clock Configuration'' panel, system clock is set to the maximum frequency of 64 MHz, which increases the SPI clock speed to 32 MHz.

## Slide 61: Middleware & Software Packs FreeRTOS
FreeRTOS component can be either be selected from Middleware (FREERTOS) or from the Software Pack (X-CUBE-FREERTOS) depending on the chosen STM32.
By default, the stack size of the default task defined by STM32CubeMx tool is equal to 128 words. The application default task required 512 words.

## Slide 62: Middleware & Software Packs FreeRTOS
Adjust heap :The size heap value should be set at least to 40Kbytes. To optimize the memory, this value could be adjusted during integration and validation tests of the application

## Slide 63: NVIC

## Slide 64: Middleware & Software Packs X-CUBE-ST67W61 Software package
Select BLE_Commissioning_v

## Slide 65: Middleware & Software Packs X-CUBE-ST67W61 Software package
Platform Settings

## Slide 66: Middleware & Software Packs X-CUBE-ST67W61 Software package
Disable W6X_POWER_SAVE_AUTO

## Slide 67: Project Creation
Here, we are enabling the Flat directory structure: (i.e. Driver and MW directories copied into your project directory)
1. Enable “Generate Under Root”
2. Enable “ Use Default Firmware Location”

## Slide 68: Project Creation
3. Enable “Copy only the necessary files”

## Slide 69: Generate Code
4. Enable this option
(here: we are not generating this function call)
5. Generate Code

## Slide 70: Folder Structure
Folder structure view after generating the code from CubeMX
App code
Core
Drivers
Middlewares
ST67W6X
Utilities

## Slide 71: STM32CubeIDE
Load the project on the STM32CubeIDE
Call main_app() function under StartDefaultTask() in main.c file

## Slide 72: xPortIsInsideInterrupt()
If the used device embeds an Arm® Cortex®M0+ (e.g. STM32G0) and its FreeRTOS version is older than of V10.6, definition below must be added manually after project has been generated.
The below function definition must be added in the portmacro.h file (Project/Middlewares/Third_Party/ FreeRTOS/ Source/Portable/ARM_CM0)
#define portINLINE __inline
#ifndef portFORCE_INLINE #define portFORCE_INLINE inline __attribute__( ( always_inline ) ) #endif
portFORCE_INLINE static BaseType_t xPortIsInsideInterrupt( void )​ {​ uint32_t ulCurrentInterrupt;​ BaseType_t xReturn;​ /* Obtain the number of the currently executing interrupt. */​ __asm volatile ( "mrs %0, ipsr" : "=r" ( ulCurrentInterrupt )::"memory" );​ if( ulCurrentInterrupt == 0 )​ {​ xReturn = pdFALSE;​ }​ else​ {​ xReturn = pdTRUE;​ }​ return xReturn;​ }

## Slide 73: STM32CubeIDE
Call xPortIsInsideInterrupt() function under portmacro.h file
IMP: As we are using G0 (CortexM0) -> older version of FreeRTOS, so we need to add this function definition manually.
#define portINLINE __inline
#ifndef portFORCE_INLINE #define portFORCE_INLINE inline __attribute__( ( always_inline ) ) #endif
portFORCE_INLINE static BaseType_t xPortIsInsideInterrupt( void )​ {​ uint32_t ulCurrentInterrupt;​ BaseType_t xReturn;​ /* Obtain the number of the currently executing interrupt. */​ __asm volatile ( "mrs %0, ipsr" : "=r" ( ulCurrentInterrupt )::"memory" );​ if( ulCurrentInterrupt == 0 )​ {​ xReturn = pdFALSE;​ }​ else​ {​ xReturn = pdTRUE;​ }​ return xReturn;​ }

## Slide 74: STM32CubeIDE
Here we are disabling the custom memcpy() definition, as we would be using the memcpy() definition in string.h
Project/ST67W6X/spi_port.c
Add #ifndef STM32G0B1xx
Add #endif

## Slide 75: Build and flash
Build the project
2. Flash the project

## Slide 76: Tera Term Logs
Tera Term Logs after flashing

## Slide 77: ST BLEToolbox/ ST BLE Webpage
To interface with the Wi-Fi commissioning embedded application, you can use STBLEToolbox Andoid/iOS application / ST Web Bluetooth® Interface
Download STBLEToolBox
The versions supporting Wi-Fi commissioning service are v1.4.3 for Android and 1.2.8 for iOS
Steps to launch and connect to Wi-Fi AP:
Launch the smartphone application and enable the scan button, if it is not already activated.
You can filter scanned devices by clicking on the SHOW FILTERS button and select ST BLE Wi-Fi to show only devices with Wi-Fi commissioning service.
Select your device, named ST_WiFi_XX where XX represents the last BD address digit, and connect to it.

## Slide 78
4. Once connected to the Bluetooth® LE device, click on Wi-Fi commissioning button to open the commissioning dedicated interface.
From this interface,
Launch a Wi-Fi scan (1),
To detect and list all available networks(2).
Once the available networks are displayed, select the one you want to connect to (2)
Type a password if needed (3)
Click on CONNECT button (4).

## Slide 79
Once the connection request is done, the connection status is displayed in the interface. Clicking on the Ping button start a ping test with the Wi-Fi access point and returns results in the interface.

## Slide 80: Walk through of the MQTT application
ST67W611M Wi-Fi® – ST67W6X_MQTT Demonstration - stm32mcu

## Slide 81: ST67W6X MQTT Overview
Description
  The MQTT demonstration available in the X-CUBE-ST67W61 expansion package implements an MQTT client which connects to an MQTT Broker in order to publish environmental sensor data and device local information and subscribe on MQTT topics to receive command.
In this example, the subscribed topic can be used to receive additional 'control’ actions from a remote client publishing to the same topic.
Change the LED state on the host board
To monitor the data sent and received, to/from the topics, a MQTT client can be installed on a PC, smartphone or tablet. Subscribing to the configured topics, allows the client to be notified every time the device publishes data to this topic.
Requirements
  A X-NUCLEO-67W61M1 Wi-Fi Expansion board.
  A NUCLEO-U575ZI-Q Host board.
  A Wi-Fi Access Point with internet access and no firewall blocking the MQTT requests.
  [Optional] A X-NUCLEO-IKS4A1 Environmental sensors expansion board.

## Slide 82: ST67W6X MQTT Topology
USB serial
PC with Hyper Terminal
Internet
Wi-Fi
Wi-Fi station
NUCLEO-U575ZI-Q X-NUCLEO-67W61M1
X-NUCLEO-IKS4A1
MQTT dashboard
MQTT Broker
Wi-Fi Access Point

## Slide 83: ST67W6X MQTT Usage
Initialization of Wi-Fi, Net and MQTT modules in the Network Coprocessor.
Wi-Fi connection establishment with the local Access Point.
Synchronization of local time in using the Network Coprocessor SNTP client.
Initialization of MEMS expansion board to get environmental sensor values.
Connection of MQTT Client to a remote MQTT broker.
MQTT topic subscription to receive messages from cloud.
Periodic publication of message including:
  Environmental sensor values**
  Local time
  RSSI of Access Point
**If MEMS board is not included these values will not be published

## Slide 84: MQTT Initialization process

## Slide 85: MQTT Application Process

## Slide 86: ST67W6X MQTT User setup
Local Access Point credentials: App_MQTT\App\app_config.h
  #define WIFI_SSID "ST_DEMO"
  #define WIFI_PASSWORD "stdemo01"
MQTT parameters: App_MQTT\App\app_config.h
  #define MQTT_HOST_NAME "broker.emqx.io"
  #define MQTT_HOST_PORT 1883
  #define MQTT_SECURITY_LEVEL 0
  #define MQTT_CLIENT_ID "mySTM32_772"
  #define MQTT_USERNAME ""
  #define MQTT_USER_PASSWORD ""
Notes :
  It uses a public broker
  Requires at least one device publisher and one subscriber
  TLS (secure broker connection)

## Slide 87: ST67W6X MQTT IoT MQTT panel app
Smartphone client : IoT MQTT Panel
  Android play store: IoT MQTT Panel - Apps on Google Play
  Android APK-pure: https://apkpure.com/iot-mqtt-panel/snr.lab.iotmqttpanel.prod
  Apple store: IoT MQTT Panel on the App Store
PC / Web client (no firewall)
  HiveMQ: MQTT Client by HiveMQ
  Mosquitto: Eclipse Mosquitto

## Slide 88
Build and flash the MQTT_App
The AP would directly connect to the ST67 with the set WIFI_SSID and WIFI_PASSWORD
Once connected the MQTT portion of the application will automatically start!
The topics (sensor, RSSI, and time) data displayed in MQTT application on smartphone, where only RSSI will be updated within the graphs.

## Slide 89: MLC - Machine Learning Core

## Slide 90: MLC - Machine Learning Core
MLC is an in-sensor classification engine based on a decision tree logic
MLC is able to increase accuracy with a better context detectability,
offloading the main processor while the built-in sensors identify motion data
SENSOR
  Accelerometer
Results
  Gyroscope
  External sensors
Digital Pre-defined Features
Filters
Meta-classifier
Sensor Data
Decision Tree
Computation Block
Main processor
Motion sensing
Notes: MLC - Machine Learning Core
a dedicated core for machine learning processing embedded inside the sensor
This means that algorithms are executed directly inside the sensor
Allows reduction of power consumption
Sensor data passes through a computation block where filters are applied and features extracted
The results are then used in a decision tree logic
A decision tree is a mathematical tool composed of a series of configurable nodes.
Each node is characterized by an “if-then-else” condition, where an input signal (represented by statistical parameters calculated from the sensor data) is evaluated against a threshold.
The results of the decision tree can be read from the application processor at any time. Furthermore, there is the possibility to generate an interrupt for every change in the result in the decision tree.

## Slide 91: ML model training
Dataset
Houses
Tokyo
The features that will be used
In which decision nodes the features will be used
The threshold values for decision nodes
The results for the leaf nodes
Training the same Machine Learning Model with another dataset (i.e. houses in Milan),
the resulting decision tree will be different in order to “best fit” the new data given for training
What the ML model learn from the data?

## Slide 92: IMU Machine Learning Core - Overview
Computation Block
Sensors Data:
  Accelerometer  [
  Gyroscope  [
  External sensor  [
  Magnitude 
Computation Block
  Sensors data can be filtered with a 2nd order IIR Filter.
  Features are statistical parameter calculated from: Input Data or Filtered Input Data
  Examples of features are: Mean, Variance, Energy, Peak to Peak, …
Decision Tree
  is a predictive model built from training data. Outputs of the computation blocks are the inputs of the decision tree.
  Each Node is characterized by one «if-then-else» condition.
      Mean on Acc_X < 0.5 g
      Variance on Gyro_Z < 200 dps
  Decision tree can either generate a result at every sample or filter the results with a Meta-classifier, to have a more robust output.
Sensors Data
Accelerometer
Gyroscope
External Sensor
Filters
Digital Pre-defined Features
Meta-classifier
Node
Decision Tree

## Slide 93: ST toolbox for machine learning core (MLC) in the sensor
Machine learning core configuration
Operating mode
Capture data
Label data
Build decision tree
Embed decision tree
Process new data
Accelerometer
Gyroscope
External sensors
Filters
Features
Real time test
DT implementation
Classification
Results
HOW
WHAT
STBLESensorr
STBLESensor
MEMS Studio
and external tools

## Slide 94: Data collection: Key points
Class 1 >> Motor stop…
Class 2 >> Motor running OK
Class 3 >> Motor running NG
Sensor configuration
Sensor selection
Class definition
Other external sensors
(Pressure, Compass, …)
Accelerometer
Gyroscope
Class 1 >> Still
Class 2 >> Walking
Class 3 >> Running
Class 4 >> Riding bicycle
Class 5 >> Car
Output Data Rate (ODR)
…
Sampling interval
Full Scale (FS)
FS
Motor vibration example
Human Activity Recognition example
Sensors Data

## Slide 95: Features calculation inside MEMS
Filters
Features
Raw data
Mean
Variance
Energy
Peak-to-Peak
Zero crossing
Positive Zero crossing
Negative Zero crossing
Peak detector
Positive Peak detector
Negative Peak detector
Minimum
Maximum
Acc_X, Acc_Y, Acc_Z
Acc_V, Acc_V2
Gyro_X, Gyro_Y, Gyro_Z
Gyro_V, Gyro_V2
ExtSens_X, ExtSens_Y, ExtSens_Z
ExtSens_V, Ext_Sens_V2
Filtered data
(High-pass, Band-pass, IIR1 and IIR2 filters)
      Note: the window for features computation (WL) is configurable (from 1 to 255 samples). It is not a moving window
Computation Block

## Slide 96: Window size selection
Window length is strongly dependent on the application
The window should capture all of the information for the decision tree to separate different classes
A few tips for selecting the right size:
Selection by the user after data analysis and visualization
If the motion is repetitive at some frequency, ideal window size should be long enough to capture the entire motion pattern
Short window length could make the response quick
Consider the slowest varying signal

## Slide 97: Decision Tree Output
Decision tree results are accessible through dedicated registers in IMU
An interrupt is generated when the decision tree result changes Interrupt status bits are available in dedicated registers
Interrupt can be routed to INT1/2 pad through dedicated register
Decision Tree

## Slide 98: MLC Configuration Demo

## Slide 99: MLC Configuration
Machine learning core configuration
Operating mode
Capture data
Label data
Build decision tree
Embed decision tree
Process new data
Accelerometer
Gyroscope
External sensors
Filters
Features
Real time test
DT implementation
Classification
Results
HOW
WHAT
X-CUBE-MEMS1
+

## Slide 100: Step 1 – Capture Data
Prepare Board for Data Capture
Use Datalog Extended Firmware from X-CUBE-MEMS1 Package
  Note: Firmware is Board Specific – use the right combo for the board stack you have
  X-CUBE-MEMS1\Projects\NUCLEO-U575ZI-Q\Examples\IKS4A1\DataLogExtended\Binary
Use STM32CubeProgrammer to flash the DatalogExtended binary to the board
Disconnect from board
Reset the board
NOTE: This section is intended to be a live demo, showing how the flow to generate mlc config file works using MEM Studio

## Slide 101: Step 1 – Capture Data
Configure Sensors for Data Capture
Open MEMS Studio
Connect to the board
Select LIS2DUXS12 as accelerometer and click select
In Quick Setup tab, select accelerometer FS=2g and ODR 12.5Hz (these match Motion Intensity example on github)
Click Save to File tab
Set log file location, e.g. C:\ST67_Workshop\MLC_Demo\
In Data box, right click then unselect all. Then check Timestamp and Accelerometer.
Ensure Time base is set to timestamp

## Slide 102: Step 1 – Capture Data
Run Data Capture
Open Line charts tab to show accel data
Click Play button (top left) to start data capture
Hold board in hand for 20s – this is motion intensity 0
Gently shake the board along all 3 axes for 20s – this is motion intensity 1
Vigorously shake the board along all 3 axes for 20s – this is motion intensity 2
Stop the capture by pressing stop button in top left corner of MEMS Studio

## Slide 103: Step 2 – Label Data
Open Data Analysis tab
Load the accel data capture file you created with the 3 types of motion
Use time domain graph
Click on graph to select regions and label Motion Intensity 0, 1 and 2: MI0, MI1, MI2
Once all 3 MI’s are labeled, click Save Labeled Data to generate 3 individual motion capture files, save them to same folder as original data capture file, e.g: C:\ST67_Workshop\MLC_Demo
Use file explorer to show that 3 files have been created with label in file name

## Slide 104: Step 3 – Build Decision Tree
Load Data Patterns
Open Advanced Features tab and select MLC
Make sure Data Patterns tab is selected
Set workspace to C:\ST67_Workshop\MLC_Demo
Select the LIS2DUXS12 sensor
Using Browse button or file explorer drag & drop to load MI0 file. Assign class label MI0 to it. Click “Load”.
Repeat above step for MI1 and MI2
You should have 3 pattern files loaded with classes MI0 through MI2

## Slide 105: Step 3 – Build Decision Tree
Configure AFS
Open AFS tab
Set Machine Learning Core Settings: ODR 12.5 to match captured data, Window length=25 (2s of data)
Configure Inputs (to match captured data)
  Accelerometer_only
  Full Scale 2g
  ODR: 12.5
Leave AFS settings at default and click Run to start automatic feature selection
Once AFS completes, click Apply to Settings to transfer filters/features to ARFF panel

## Slide 106: Step 3 – Build Decision Tree
ARFF Generation
Open ARFF Generation tab
Note settings from AFS have been set, review them
Click Generate ARFF File to generate the ARFF file used in the next step (DT generation)

## Slide 107: Step 3 – Build Decision Tree
Decision Tree Generation
Open Decision Tree Generation tab
Set number of decision trees to 1
Click Generate Decision Tree
Once DT is generated review results and show generated decision tree (show Dectree button)

## Slide 108: Step 3 – Build Decision Tree
Generation of Configuration Files
Open Config generation tab
For output values for the classes select 0, 1 and 2 to match MI0,1 and 2
Leave counters at 0
Click Generate Config file
Show json file
Click Export to show how to generate corresponding header file

## Slide 109: Step 3 – Build Decision Tree
Test Generated Tree
Click Load Config into Sensor
Click Decision Tree Output Viewer
Press Play button to start data capture/testing
Show Motion Intensities 0, 1 and 2

## Slide 110: Hands-On: Embed MLC into MQTT App

## Slide 111: Enabling MLC in Your STM32 Project
In this hands-on part of the workshop, we’ll use a generated MLC example available on ST’s github
Github: https://github.com/STMicroelectronics/st-mems-machine-learning-core
We’ll use the LIS2DUXS12 sensor

## Slide 112: Enabling MLC in Your STM32 Project
The README file provides useful information for integration
Overview, Sensor configuration, MLC outputs, interrupts

## Slide 113: Enabling MLC in Your STM32 Project
Folder contains 3 files:
  README.md – useful info
  JSON cofig file – useful for testing using ST Tools e.g MEMS Studio
  C header file – useful for integration into STM32 projects
We’ll use the header file to enable the MLC in out MQTT Project
We’ll send the detected motion intensity to the MQTT broker and display it in the mobile app

## Slide 114: Enabling MLC in Your STM32 Project
Header file contains an array with a sequence of commands to execute to configure the sensor and MLC
Each array entry contains an opcode and relevant info, such as register addresses and data

## Slide 115: Enabling MLC in Your STM32 Project
We’ve added the necessary code to configure the MLC, read the outputs and publish the motion intensity to the MQTT broker
Modified files:
  Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT\X-CUBE-MEMS1\App\sys_sensors.h
  Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT\X-CUBE-MEMS1\App\sys_sensors.c
  Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT\App_MQTT\App\app_config.h
  Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT\App_MQTT\App\main_app.c

## Slide 116: Enabling MLC in Your STM32 Project
Modified files: sys_sensors.h

## Slide 117: Enabling MLC in Your STM32 Project
Modified files: sys_sensors.c
#include "logging.h"
#include "iks4a1_motion_sensors_ex.h"
#include "lis2duxs12_motion_intensity.h" /* MLC Config file */
/* Private function prototypes -----------------------------------------------*/
static int32_t MLC_Init(void);
int32_t Sys_Sensors_Read(Sys_Sensors_Data_t *data)
{
…
#ifdef USE_MLC
/* Get mlc outputs */
(void)IKS4A1_MOTION_SENSOR_Write_Register(IKS4A1_LIS2DUXS12_0, LIS2DUXS12_FUNC_CFG_ACCESS, 0x80);
(void)IKS4A1_MOTION_SENSOR_Read_Register(IKS4A1_LIS2DUXS12_0, LIS2DUXS12_MLC1_SRC, &data->motion_intensity);
(void)IKS4A1_MOTION_SENSOR_Write_Register(IKS4A1_LIS2DUXS12_0, LIS2DUXS12_FUNC_CFG_ACCESS, 0x00);
#endif
…
}

## Slide 118: Enabling MLC in Your STM32 Project
Modified files: sys_sensors.c
static int32_t Sys_Sensors_IKS4A1_Init(void)
{
…
#ifdef USE_MLC
/* Initialize the MLC */
ret = MLC_Init();
#endif
…
}

## Slide 119: Enabling MLC in Your STM32 Project
Modified files: sys_sensors.c
int32_t MLC_Init(void)
{
…
length = MEMS_CONF_ARRAY_LEN(MLC_CONFIGURATION);
i = 0;
while ((i < length) & (ret == BSP_ERROR_NONE))
{
if (MLC_CONFIGURATION[i].type == MEMS_CONF_OP_TYPE_DELAY)
{
HAL_Delay(MLC_CONFIGURATION[i].data);
}
else if (MLC_CONFIGURATION[i].type == MEMS_CONF_OP_TYPE_WRITE)
{
ret = IKS4A1_MOTION_SENSOR_Write_Register(IKS4A1_LIS2DUXS12_0, MLC_CONFIGURATION[i].address, MLC_CONFIGURATION[i].data);
}
else
{
/* Unsupported opcode */
ret = BSP_ERROR_FEATURE_NOT_SUPPORTED;
}
i++;
}
…
}

## Slide 120: Enabling MLC in Your STM32 Project
Modified files: app_config.h
/* Local Access Point (e.g. gateway, hotspot, etc) connection parameters */
#define WIFI_SSID “<wifi-ssid>"
#define WIFI_PASSWORD “<wifi-password>"
/** Host name of remote MQTT Broker
* Multiple options are possibles:
* - broker.hivemq.com
* - broker.emqx.io
* - test.mosquitto.org
*/
#define MQTT_HOST_NAME "broker.hivemq.com"
/** Port of remote MQTT Broker */
#define MQTT_HOST_PORT 1883
/** Security level. only non-secure is currently available */
#define MQTT_SECURITY_LEVEL 0
/** MQTT Client ID to be identified on MQTT Broker */
#define MQTT_CLIENT_ID “<your-client-id>"

## Slide 121: Enabling MLC in Your STM32 Project
Injecting Client ID into IotMQTTPanel config file:
Open a command prompt
cd to
Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT\resources>
Run the command:
IotMQTTPanel_Helper.py IoTMQTTPanel-250618_134546.json --clientid <Your ClientID> -- broker <MQTT broker> -o IotMQTTPanel-MLC-MotionIntensity.json
Copy the output file IotMQTTPanel-MLC-MotionIntensity.json to your mobile device
Load the configuration file into the IotMQTTPanel app

## Slide 122: Enabling MLC in Your STM32 Project
Modified files: main_app.c
static void Subscription_process_task(void *arg)
{
…
/* Process the field 'motionintensity'. Value type: Int. Format: 1 (range 0-7) */
json = cJSON_GetObjectItemCaseSensitive(child, "motionintensity");
if (json != NULL)
{
if (cJSON_IsNumber(json) == true)
{
LogInfo(" %s: %d\n", json->string, json->valueint);
}
else
{
LogError("JSON parsing error of %s value.\n", json->string);
}
}
…
}

## Slide 123: Enabling MLC in Your STM32 Project
Modified files: main_app.c
#ifdef USE_MLC
len += snprintf((char *)&mqtt_pubmsg[len], MQTT_MSG_BUFFER_SIZE - len,
", \"temperature\": %.2f, \"humidity\": %.2f, \"pressure\": %.2f, \"motionintensity\":%d",
(double)sensors_data.temperature, (double)sensors_data.humidity, (double)sensors_data.pressure, (int)sensors_data.motion_intensity);
#else
len += snprintf((char *)&mqtt_pubmsg[len], MQTT_MSG_BUFFER_SIZE - len,
", \"temperature\": %.2f, \"humidity\": %.2f, \"pressure\": %.2f",
(double)sensors_data.temperature, (double)sensors_data.humidity, (double)sensors_data.pressure);
#endif

## Slide 124: Enabling MLC in Your STM32 Project
Modified files: main_app.c
static void Subscription_process_task(void *arg)
{
…
/* Process the field 'motionintensity'. Value type: Int. Format: 1 (range 0-7) */
json = cJSON_GetObjectItemCaseSensitive(child, "motionintensity");
if (json != NULL)
{
if (cJSON_IsNumber(json) == true)
{
LogInfo(" %s: %d\n", json->string, json->valueint);
}
else
{
LogError("JSON parsing error of %s value.\n", json->string);
}
}
…
}

## Slide 125: Enabling MLC in Your STM32 Project
To enable the MLC code, add USE_MLC to project properties

## Slide 126: Enabling MLC in Your STM32 Project
Build the project
Make sure project builds successfully

## Slide 127: Enabling MLC in Your STM32 Project
Flash the board

## Slide 128: Enabling MLC in Your STM32 Project
Connect to board using Tera Term

## Slide 129: Enabling MLC in Your STM32 Project
Open the IotMQTTPanel app and load the configuration file you generated
Move/shake the board to see motion intensity value change in the Backup panel

## Slide 130: Hands-On: Integrating Embed MLC into MQTTS

## Slide 131: ST67W6X MQTT Hands-On
In this hands-on we will use a modified MQTT project that includes the MLC portion as well as additional resources located on GitHub
STMicroDEMO/ST67W6X_MQTT_MLC
Download the project from GitHub and save the file uncompressed within the X-Cube package:
  C:\X_CUBE_ST67W61_V1.0.0\Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X
**Note: GitHub may save the project as “ST67W6X_MQTT_MLC-main”

## Slide 132: ST67W6X MQTT Higher security schemes
Higher level security schemes can be enabled to utilize TLS to prevent third party interception of data when publishing data to the cloud.
Security Schemes:
  0 - MQTT over TCP with no authentication and no encryption
  1 - MQTT over TLS with username authentication
  2 - MQTT over TLS with server certificate
  3 - MQTT over TLS with client certificate
  4 - MQTT over TLS with both certificates
The different configurations must be followed when configuring the broker and client.
mqtt_connect structure that must be configured for each MQTT use case.

## Slide 133: ST67W6X MQTT Enabling Higher security schemes
When enabling security schemes 2 or higher, certificates and keys must be provided to verify security credentials.
The NCP utilizes littlefs to read certificates and keys from the host MCU that are then stored internally.
To load certificates and keys onto the host MCU, desired certificates and keys must be placed within the lfs folder in the MQTT demonstration folder:
  Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT\littlefs\lfs
The desired certificates and keys are loaded onto the host MCU as a littlefs.bin using linker input specified in the project settings.
This binary can be built from the user specified certificates and keys using the build.bat script once the certificates and keys are placed in the lfs folder.
MQTT Security and Certificates

## Slide 134: ST67W6X MQTT ST67 Client Setup - Security Scheme 1
In this hands-on portion of the work-shop TLS will be utilized within the MQTT demo using security scheme 1.
Security scheme 1 - MQTT over TLS with username and password
MQTT Local Client configuration – Setup on ST67 within CubeIDE in app_config.h

## Slide 135: ST67W6X MQTT Import Project into STM32CubeIDE
Import the modified MQTT application into CubeIDE
Select “File”
Select “Import…”

## Slide 136: ST67W6X MQTT Import Project into STM32CubeIDE
Select “Exisiting Projects into Workspace”
Select “Next”

## Slide 137: ST67W6X MQTT Import Project into STM32CubeIDE
Select “Browse…”
Navigate to “C:\ x-cube-st67w61-v1.0.0\Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT_MLC”
Select “Finish”

## Slide 138: ST67W6X MQTT Project into STM32CubeIDE
Project Structure:
Application – Contains the files for the application functionality (i.e. main.c, main_app.c, sys_sensors.c, etc.)
Drivers – Contains the HAL driver, CMSIS, and BSP libraries for STM32U575 and IKS4A1.
Middlewares – Contains the network driver libraries for the ST67 modules.
Utilities – Contains the stm32_lpm.c file.

## Slide 139: ST67W6X MQTT Project into STM32CubeIDE
Open app_config.h:
Open the file main_app.c found in the Application library under User/App_MQTT/App.
With main_app.c open, to open app_config.h, “right-click” and select “Open Declaration” on app_config.h or hold CTRL and “left-click” on app_config.h.**
**Note: You must first try building the application to open the file by selecting “Open Declaration”.

## Slide 140: ST67W6X MQTT ST67 Client Setup - Security Scheme 1
Modified app_config.h to enable security scheme 1
Modifying the port to 8883 corresponding to TLS rather than TCP
Security scheme set to 1 corresponding to use username and password fields
Specified to unique client ID (not necessary for when enabling security)
Specified username, please avoid username with spaces
Specified password

## Slide 141: ST67W6X MQTT ST67 Client Setup - Security Scheme 1
Modified app_config.h to provide access point credentials
Once modified with these security changes and with the changes made to enable to MLC portion, save the project and build the application.
Make sure project builds successfully
Note: SSID cannot have special characters, and both SSID and password should not have spaces

## Slide 142: ST67W6X MQTT Nucleo-U575ZI-Q Serial Terminal Output
Application running and displaying messages on serial terminal and expected output:
See FW versions for both host MCU and ST67W6X
Module initializations (i.e. Wi-Fi, Net, MQTT)
Scan and connection to AP
MEMS Init
MQTT Configure
MQTT Publish and Subscription received

## Slide 143: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
The IoT MQTT Panel application must be modified to use a username and password as well as match user specifications.
The IoTMQTTPanel-MLC-MotionIntensity.json is used to configure the IoT MQTT Panel application.

## Slide 144: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
The .json file can be modified quickly to match the user’s specifications using the IoTMQTTPanel_Helper.py script.
  The Python script is located within the project directory at:
    Projects\NUCLEO-U575ZI-Q\Demonstrations\ST67W6X\ST67W6X_MQTT_MLC\resources

## Slide 145: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
A command window can be opened at the directory containing the python script by typing in “cmd” in the address bar of the file explorer window.

## Slide 146: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
To see the available parameters that can be edited within the IoTMQTTPanel_Helper.py provide the option ‘-h’ when calling the script

## Slide 147: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
When calling the script the JSONin file must be specified
For this hands-on we will be using the IotMQTTPanel-MLC-MotionIntensity.json
We also recommend specifying the “out” file which will save any changes specified in the python script to another .json file

## Slide 148: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
Configure the .json file with the configurations specified in app_config.h

## Slide 149: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
Setup MQTT Client on IoT MQTT Panel Application
Load modified .json file onto smart device
Restore connection based on configurations set in .json file
Verify connection and data in app with application running on STM32U5+ST67
NewPanel.json

## Slide 150: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
Modified .json file must be provided to a mobile device with IoT MQTT Panel installed
  Recommended method is to use a personal email to send the file to your mobile device.
NewPanel.json

## Slide 151: ST67W6X MQTT IoT MQTT Panel Client Setup – Connection Setup
With IoT MQTT Panel Application open select “Connections” to bring up MQTT Panel application menu.

## Slide 152: ST67W6X MQTT IoT MQTT Panel Client Setup – Connection Setup
Select “Backup and Restore” to “Backup” an existing connection or “Restore” a preconfigured connection.

## Slide 153: ST67W6X MQTT IoT MQTT Panel Client Setup – Connection Setup
Select “Restore” to bringup file storage and select preconfigured .json file stored within smart device’s memory

## Slide 154: ST67W6X MQTT IoT MQTT Panel Client Setup – Connection Setup
With preconfigured .json file selected, the IoT MQTT Panel application will “Alert!” the user regarding same client-id.
Select “Yes”.
  Client-ID referred to here is correlated to the connection. Client-ID configured previously in the .json and app_config.h is correlated to the topic data is published under.

## Slide 155: ST67W6X MQTT IoT MQTT Panel Client Setup - Security Scheme 1
The main dashboard:
  Display the graphical values of RSSI, Temperature, Humidity and Pressure from device published message
  The Green LED statues on the NUCLEO-U575 Host board can be managed through Button panel
The backup dashboard:
  Display the graphical values of Humidity, Temperature and Motion Intensity

## Slide 156: Documentation

## Slide 157: Wifi wiki
Access:
The wifi wiki is opened to all
Wiki address of the main page
https://wiki.st.com/stm32mcu/wiki/Connectivity:Introduction_to_Wi-Fi
We will be happy to get your feedback!

## Slide 158: Wiki Wi-Fi®: pages breakdown
  About Wi-Fi
  Details about ST67W611M1
  X-CUBE-ST67W61
  Host boards supported
  Tools & References

## Slide 159: Other documentation
Getting started with X-CUBE-ST67W61 here
MW API documentation is available:
  X-CUBE-ST67W61_V1.0.0\Middlewares\ST\ST67W6X_Network_Driver\Doc\ST67W6X_Network_Driver.chm

## Slide 160: ST Customer Support
ST Support Home
  Tickets can be submitted under the part number X-CUBE-ST67W61 or ST67W611M1

## Slide 161
Find out more at www.st.com

## Slide 162
For further support in creating a PowerPoint presentation, including graphic assets, formatting tools and additional information on the ST brand
you can visit the ST Brand Portal https://brandportal.st.com
Please remove this page
before publishing the
presentation

## Slide 163: Backup Slides